## Slide 1
01
Cisco 7945G
Home telephony
Asterisk in k3s + Home Assistant
10 phones with color displays
Notes: The purchased lot contained 10 Cisco 7945G phones. The eBay delivery email dated December 1, 2022 confirms the model. Shipping and payment details are excluded from the repository. Inventory each remaining phone to establish its condition and firmware. Updated October 17, 2026. These slides describe the architecture and deployment process. Actual installation and call results belong in the separate acceptance record.

## Slide 2
Our lot: 10 Cisco 7945G phones
02
10
phones
7945_7965 SIP firmware family
A phone running SCCP needs SIP firmware.
This model does not need MPP conversion.
Before starting
Record PID, VID/HW, MAC, App Load,
Boot Load, IP and TFTP for every phone.
Notes: The eBay delivery email dated December 1, 2022 confirms the model and quantity. Cisco firmware family 7945_7965: https://www.cisco.com/web/software/282074288/128566/cmterm-7945_7965-sip.9-4-2SR2-2-readme.html
PoE: https://www.cisco.com/c/en/us/support/docs/voice-unified-communications/unified-ip-phone-7900-series/97869-poe-requirement-faq.html
Cisco provides SIP firmware for this model. Verify the required Asterisk features on the pilot phone.

## Slide 3
Cisco, Asterisk and Home Assistant
03
10 × Cisco 7945G
PoE 802.3af
PoE switch
Voice LAN / VLAN
Asterisk / PJSIP
static IP
Router
DHCP option 150
Temporary TFTP
firmware and XML
Home Assistant
AMI + VoIP / Assist
Ethernet
SIP / RTP
DHCP
download
AMI
SIP / RTP
Asterisk uses hostNetwork and one replica. HA opens the AMI connection to the PBX.
TFTP runs only during provisioning. SIP, RTP and AMI stay on the LAN / VPN.
Notes: The design uses one Asterisk replica on a designated LAN node with hostNetwork and a static LAN IP. Keep the existing router DHCP service. Run TFTP only when needed. HA opens TCP AMI to Asterisk. For Assist, Asterisk opens SIP to HA VoIP and audio flows in both directions. Home Assistant may run on another LAN node or across the existing VPN. HTTP Ingress does not transport these protocols. Kubernetes: https://kubernetes.io/docs/concepts/workloads/controllers/deployment/
PJSIP: https://docs.asterisk.org/Configuration/Channel-Drivers/SIP/Configuring-res_pjsip/res_pjsip-Configuration-Examples/
HA: https://github.com/ha-homelab/asterisk-telephony
VoIP: https://www.home-assistant.io/integrations/voip/
See docs/k3s-deployment.md and docs/home-assistant.md.

## Slide 4
Signaling and audio ports
04
5060
TCP / UDP
SIP: Cisco TCP, HA UDP
10000–10199
UDP on PBX
RTP / audio
5038
TCP on PBX
AMI: HA source IP /32
69 + 20000–20031
UDP on PBX
Temporary TFTP
HA uses dynamic RTP / RTCP ports. Restrict firewall rules to the required source IPs.
Notes: PBX ports in this project: SIP TCP 5060 by default, optional UDP 5060, RTP UDP 10000–10199. tftpd-hpa uses UDP 69 and UDP 20000–20031. Allow AMI TCP 5038 only from the actual HA source IP/32. HA VoIP listens on SIP UDP 5060 or the selected port, plus dynamic RTP/RTCP UDP ports restricted to the PBX. Cisco RTP uses UDP 16384–16482. Firewall rules must account for both directions. NetworkPolicy alone does not protect hostNetwork. PJSIP: https://docs.asterisk.org/Configuration/Channel-Drivers/SIP/Configuring-res_pjsip/res_pjsip-Configuration-Examples/
VoIP: https://www.home-assistant.io/integrations/voip/
See docs/home-assistant.md.

## Slide 5
7945G has built-in PoE support
05
PoE switch
IEEE 802.3af
Cisco 7945G
SW / Network port
Standard switch
Ethernet
Active injector
IEEE 802.3af
Cisco 7945G
SW / Network port
data + power
data
PoE
A passive 24 V injector is unsuitable. The UPS also needs to power the switch, router and k3s node.
Notes: Cisco 7945G supports IEEE 802.3af: https://www.cisco.com/c/en/us/support/docs/voice-unified-communications/unified-ip-phone-7900-series/97869-poe-requirement-faq.html
If the existing switch does not supply PoE, use an active IEEE 802.3af injector or a PoE switch. The phone needs no hardware modification. Connect to the SW/Network port. Check the per-port and total switch power budgets. To maintain service during a power outage, the UPS must power the entire network path.

## Slide 6
One pilot phone before the full fleet
06
Inventory
PID / HW / Load
Firmware path
SCCP to SIP
TFTP ready
bundle + SEP XML
One pilot phone
stable power
Call tests
audio / DTMF / reboot
Remaining phones
one at a time
HW 13.0+ requires at least 9.3(1)SR3. The upgrade path depends on the current load.
Prepare TFTP and recovery before a reset. Keep power connected during flash writes.
Notes: The appropriate reset procedure depends on the current phone state. Check App Load and the required upgrade path first. Cisco README for the 7945_7965 family: https://www.cisco.com/web/software/282074288/128566/cmterm-7945_7965-sip.9-4-2SR2-2-readme.html
Never downgrade HW 13.0+ below 9.3(1)SR3. Do not apply an intermediate 8.5(2) load to the entire fleet. Phones starting below 8.3(3) require an intermediate 8.3(3)–8.5(2) load before 9.3(1)+, subject to the selected release notes: https://www.cisco.com/en/US/docs/voice_ip_comm/cuipph/7900_series/firmware/9_3_1SR4/english/release_notes/P790_BK_RF3660D6_00_rn-9_3_1sr4-7900-series_chapter_00.pdf
Obtain the Cisco bundle from an authorized source and record its SHA-256 locally. The .loads file alone is insufficient.

## Slide 7
TFTP preparation before restart
07
Complete official firmware bundle
.loads and every referenced binary file
with the original filenames and letter case
SEP<MAC>.cnf.xml
SIP server, extension and a unique password
Load ID from the selected 7945_7965 firmware branch
Use DHCP option 150 on the home router or Alternate TFTP on the phone.
Notes: Cisco: https://www.cisco.com/web/software/282074288/128566/cmterm-7945_7965-sip.9-4-2SR2-2-readme.html
Choose the exact loadInformation value from the selected bundle README and .loads file. Do not substitute a 7942/7962 file. SEP filenames use the uppercase MAC address without separators. The configuration may contain a SIP password, so restrict TFTP to the trusted LAN. Configure DHCP option 150 on the existing DHCP server, or use Alternate TFTP on the phone.

## Slide 8
Asterisk: one extension per phone
08
201
202
…210
TCP with a separate endpoint, auth and AOR
A unique password for each phone
G.711 ulaw / alaw
direct_media=no keeps RTP on Asterisk
600 echo, 601 tone, 620 ring group. Extension 630 requires Assist.
Notes: PJSIP examples: https://docs.asterisk.org/Configuration/Channel-Drivers/SIP/Configuring-res_pjsip/res_pjsip-Configuration-Examples/
Project baseline: a separate endpoint, auth and AOR for each phone, a unique password, and matching transport in the phone XML. TCP is the default. Enable UDP for phones explicitly. Use G.711 ulaw/alaw and direct_media=no to keep RTP flowing through Asterisk. Add NAT settings only when needed. The initial configuration supports internal calls without a PSTN/SIP trunk. Test extensions: 600 echo, 601 tone, 620 ring group, and 630 Assist when HA integration is enabled.

## Slide 9
AMI: status and call control
09
Home Assistant connects to PBX:5038
Status, connected line and DTMF
Actual entity IDs from your HA instance
Place calls and hang up a specific channel
asterisk.send_action: Originate / Hangup
The DTMF example sends a harmless notification
Use a separate secret and a /32 ACL. The system permission allows administrative actions.
Notes: HA installation and package: https://github.com/ha-homelab/asterisk-telephony
Verified TECH7Fox Asterisk integration v1.0.5, pinned commit: https://github.com/TECH7Fox/asterisk-hass-integration/tree/65ea9d637a58d6edb3b2bc9e8a6f90de896a9b3e
HA opens TCP 5038 to the PBX without TLS. Restrict access to the actual source IP/32 over LAN or VPN. Keep the separate .local/ha-ami-secret.json credentials out of Git and phone XML. Permissions are read=call,dtmf and write=system, plus originate only with allow_originate:true. Upstream needs system for discovery, but that permission also allows Hangup and other administrative actions. This is privileged access. HA exposes one global asterisk.send_action service without multi-PBX selection. DTMF uses a timestamp state and Digit attribute. Sent/Received directions are relative to Asterisk. Registered derives from DeviceState and does not replace pjsip show contacts. Map actual entity IDs and verify with two phones.

## Slide 10
630: voice assistant on the phone
10
Cisco 7945G
extension 201
G.711
Asterisk
G.711 ↔ Opus
extension 630
Home Assistant
VoIP / Assist
Opus
SIP TCP
RTP
SIP UDP
RTP
First call: enable Allow calls and select a pipeline in HA.
Then test speech recognition, the spoken reply and hangup.
SIP From retains the phone extension. HA uses dynamic UDP ports for RTP / RTCP.
A call on the pilot phone verifies audio. Pod readiness checks server components.
Notes: Official HA VoIP integration: https://www.home-assistant.io/integrations/voip/
Installation and acceptance: https://github.com/ha-homelab/asterisk-telephony
Pinned Opus transcoder: https://github.com/wazo-platform/wazo-codec-opus-open-source/tree/591b6cd9b75e2b9b6d815ef364a385fccee595a7
Cisco 7945G uses G.711. The verified HA 2026.10.2 VoIP integration requires Opus. Asterisk transcodes audio in both directions through a module built from Wazo source. Translation-path and container smoke tests verify server components. Verify a real conversation on the household phone separately. SIP to Cisco defaults to TCP 5060. SIP to HA uses UDP 5060 or the selected port. PBX RTP uses 10000–10199. HA uses dynamic RTP/RTCP UDP ports. Enable Allow calls and select the pipeline for the discovered VoIP device. SIP From preserves the extension, including calls originated from HA. Test STT, the TTS reply, hangup and a repeat call. AMI carries events and commands, not audio.

## Slide 11
Deployment and commissioning
11
01
Server bootstrap
Images, static IP, firewall, Asterisk and Opus
02
Verified pilot phone
PID / HW / Load / MAC, SIP profile, temporary TFTP
03
Home Assistant setup
AMI /32, secret, actual entity IDs and VoIP pipeline
04
Acceptance and rollout
Two phones, a call to 630, then the remaining phones
Notes: See README.md, docs/pbx-bootstrap.md, docs/k3s-deployment.md, docs/home-assistant.md, scripts/ and deploy/. Namespace: telephony. Bootstrap prepares server components, images and network rules before connecting an inventoried phone. provision.py --pbx-only performs this step without fake MAC addresses, phone endpoints or TFTP. Keep allow_originate:false and assist.enabled:false until the connection prerequisites pass. Do not commit local site, inventory or secrets. TFTP requires an actual phone inventory and suitable verified firmware. Take the exact generation and deployment commands from the current runbook. One Asterisk replica with Recreate prevents hostNetwork port conflicts. Stage the HA component before a separate installation window on the existing HA instance. k3s: https://docs.k3s.io/installation/requirements
HA: https://github.com/ha-homelab/asterisk-telephony

## Slide 12
Acceptance tests on real phones
12
Telephony
201 and 202: registration, two-way audio, hold / transfer
Home Assistant
States, Originate, Hangup on the correct Channel, DTMF
Assist 630
Speech recognition, spoken reply and hangup
Repeat after phone, PBX and HA restarts. Readiness does not verify audio.
Notes: These are project acceptance criteria. Record actual household installation results separately. Use two physical phones with verified inventory. Check pjsip show contacts, calls from 201 to 202 and from 202 to 201, two-way audio, DTMF/echo, hold/transfer and the clock. Then check HA states, Originate, Hangup using the actual active Channel, and a harmless DTMF notification. Determine DTMF Sent/Received direction on the pilot. For 630: Allow calls, pipeline selection, a separate identity for each phone, STT, TTS and hangup. Repeat after a phone cold boot and controlled PBX/HA restarts. Automated runtime and smoke tests do not replace physical acceptance. https://github.com/ha-homelab/asterisk-telephony/blob/main/docs/acceptance.md

## Slide 13
Operations and recovery
13
Private backups outside Git
Inventory, SIP / AMI secrets and Asterisk data
HA config / .storage, entity mappings and image versions
One node is a single point of failure
UPS for network equipment and the k3s node
A recovery plan that preserves the LAN IP
Exclude raw DTMF and connected-line data from Recorder. Review existing history separately.
Notes: Project operating requirements: telephony runs on one node without high availability. Back up inventory, SIP/AMI secrets, configuration, persistent Asterisk data, firmware provenance, HA config/.storage and entity mappings. Test restoration separately. Do not publish SIP/AMI passwords or firmware binaries. Exclude raw DTMF and call sensors from HA Recorder. Exclusions do not remove existing history. Setting home_assistant.enabled:false and regenerating/applying the configuration disables AMI and extension 630 while retaining basic internal calls. See docs/operations.md and https://github.com/ha-homelab/asterisk-telephony/blob/main/docs/privacy.md

## Slide 14
Server readiness and phone acceptance
14
Server preparation can come first
Images, configuration, AMI and Opus
Tests verify the server components
A pilot verifies the phone experience
Phone inventory, a two-party call and Assist
Add the remaining phones after acceptance
Physical acceptance is a separate step. Keep the results in the private deployment log.
Notes: Record actual hardware results in a separate private acceptance log. These slides describe preparation and acceptance criteria. Inventory the surviving devices to record PID/HW/MAC, App Load, network addresses and power. Automated tests verify components and configuration. Physical acceptance covers audio, HA call control, DTMF and Assist on real phones. After the pilot passes, add the remaining phones one at a time.